NATIONAL ANNEX

TO

CYS EN 1998-4:2006 Eurocode 8: Design of structures for earthquake resistance

Part 4: Silos, tanks and pipelines

PUBLIC ENQUIRY DRAFT

Prepared by: CYS/TC18

Cyprus Organisation of Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS/TC18 Committee of the Cyprus Organisation of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1998-4:2006

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1998-4:2006 where National choice is allowed (see Section NA 2)

1.1(4)

2.1.2(4)P

2.1.3(5)P

2.1.4(8)

2.2(3)

2.3.3.3(2)P

2.5.2(3)P

3.1(2)P

4.5.1.3(3)

4.5.2.3(2)P

Decisions on the use of the Informative Annexes A and B (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1998-4:2006.  In this National Annex such information is provided for the following clauses in CYS EN 1998-4:2006 (see Section NA 4)

# NATIONALLY DETERMINED PARAMETERS

## Clause 1.1 (4) Scope of CYS EN 1998-4:2006

For the design of facilities associated with large risks to the population or the environment the recommendations of other National Annexes may be used.

## Clause 2.1.2 (4)P Ultimate limit state

For the ultimate limit state, the value of the reference return period, TNCR, is 475 years.

## Clause 2.1.3 (5)P Damage limitation state

For the damage limitation state, the value of the probability of exceedance, PDLR, is 10% and the return period, TDLR, is 95 years.

## Clause 2.1.4 (8) Reliability differentiation

The value of the importance factor γI for silos, tanks and pipelines is:

- Importance Class I, γI =0,8

- Importance Class II, γI =1,0

- Importance Class III, γI =1,2

- Importance Class IV, γI =1,6

## Clause 2.2 (3) Reduction factor at damage limitation state

The reduction factor ν that may be applied to the design seismic action is:

- Importance Class I and II, ν =0,5

- Importance Class III and IV, ν =0,4

In a specific area a different value of the reduction factor ν may be used if this value is justified by special zoning studies.

## Clause 2.3.3.3 (2)P Foundation damping

The maximum value of radiation damping ξmax for soil-structure interaction analysis is 25%. Further guidance for the selection and use of damping values associated with different foundation motions is provided in the CYS EN 1998-6:2005.

## Clause 2.5.2 (3)P Combination of seismic action with other actions

The value of factor φ that must be multiplied with the combination coefficient ψEi is:

- φ =1 for full silo, tank or pipeline

- φ =0 for empty silo, tank or pipeline

## Clause 3.1 (2)P Introduction – Unit weights

The unit weights of the particulate solid stored in silos is the upper value of the unit weight listed in the CYS EN 1991-4:2006, Table E1.

For materials not listed in the table thorough tests must be carried out to determine the lower and upper value of the unit weight.

## Clause 4.5.1.3 (3) Piping – amplification factor

The value of the amplification factor γp1 on forces transmitted by the piping to the region of the tank where the piping is attached is γp1=1,3.

## Clause 4.5.2.3 (2)P Piping – overstrength factor

The value of the overstrength factor γp2 that must be taken into account on the design resistance of the piping is γp2 =1,3.

# DECISION ON USE OF THE INFORMATIVE ANNEXES A AND B

## Annex A

Annex A may be used

## Annex B

Annex B may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None