NATIONAL ANNEX

TO

CYS EN 1998-5:2004 Eurocode 8: Design of structures for earthquake resistance

Part 5: Foundations, retaining structures and

geotechnical aspects

PUBLIC ENQUIRY DRAFT

Prepared by: CYS/TC18

Cyprus Organisation of Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS/TC18 Committee of the Cyprus Organisation of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1998-5:2004

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1998-5:2004 where National choice is allowed (see Section NA 2)

1.1(4)

3.1(3)

4.1.4(11)

5.2(2)c)

Decisions on the use of the Informative Annexes A, C, D, and F (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1998-5:2004.  In this National Annex such information is provided for the following clauses in CYS EN 1998-5:2004 (see Section NA 4)

# NATIONALLY DETERMINED PARAMETERS

## Clause 1.1 (4) Scope of CYS EN 1998-5:2004

Annexes A, C, D and F are informative and may be used in the design of geotechnical aspects.

## Clause 3.1 (3) Partial factors for materials

The partial factors for the following soil strength parameters are:

- Undrained shear strength cu is γcu =1,4.

- Cyclic undrained shear strength τcy,u is γtcy =1,25.

- Unconfined compressive strength qu is γqu =1,4.

- The tangent of the angle of shearing resistance in terms of effective stress tanφ΄ is γφ΄ =1,25.

## Clause 4.1.4 (11) Reduction factor at damage limitation state

To achieve a safety factor of 1,25, the earthquake induced shear must not exceed λ =0,8 of the critical stress known to have caused liquefaction in previous earthquakes.

## Clause 5.2 (2)c) Reduction of peak ground acceleration

If it is justified by an appropriate study, the value of the peak ground acceleration α·S can be decreased to p·α·S. The value of p can not be lower than p = 0,65.

# DECISION ON USE OF THE INFORMATIVE ANNEXES A, B, C, D, E AND F

## Annex A

Annex A may be used.

## Annex C

Annex C may be used.

## Annex D

Annex D may be used.

## Annex F

Annex F may be used.

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None