NATIONAL ANNEX

TO

CYS EN 1992-3:2006

Eurocode 2: Design of concrete structures

Part3: Liquid retaining and containment structures

Public Enquiry Draft

Period of Enquiry

Prepared by: CYS TC18 EUROCODES COMMITTEE

Cyprus Organisation for Standardisation

INTRODUCTION

This National Annex has been prepared by CYS TC 18 Standardisation Technical Committee of Cyprus Organisation for Standardisation

# SCOPE

This National Annex is to be used together with CYS EN 1992-3:2006. Any reference in the rest of this text to CYS EN 1992-3:2006 means the above document.

This National Annex gives

(a)	Nationally determined parameters for the following clauses of CYS EN 1992-3:2006 where National choice is allowed (see Section NA 2)

7.3.1 (111)

7.3.1 (112)

7.3.3

8.10.1.3 (102) and (103)

9.11.1 (102)

- Decisions on the use of the Informative Annexes K, L, M and N (see Section NA 3)

- References to non-contradictory complementary information to assist the user to apply CYS EN 1992-3:2006.  In this National Annex such information is provided for the following clauses in CYS EN 1992-3:2006 (see Section NA 4)

# NATIONALLY DETERMINED PARAMETERS

## Clause 7.3.1 (111) Cracking - General considerations

The values of wk1 for structures retaining water are defined as a function of the ratio of the hydrostatic pressure, hD to the wall thickness of the containing structure, h.  For hD/h ( 5, wk1 = 0,2 mm while for hD/h ( 35, wk1 = 0,05 mm. For intermediate values of hD/h, linear interpolation between 0,2 and 0,05 should be used.

## Clause 7.3.1 (112) Cracking - General considerations

The value for xmin is the lesser of 50 mm or 0,2h where h is the element thickness.

### NA 2.3    Clause 7.3.3 Control of cracking without direct calculation

Where the minimum reinforcement given by 7.3.2 is provided, Figures 7.103N and 7.104N give values of maximum bar diameters and bar spacings for various design crack widths for sections totally in tension.

### NA 2.4    Clause 8.10.1.3 (102) and (103) Post-tension ducts

The value of k is specified as 0, 25.

## NA 2.5    Clause 9.11.1 (102) Minimum area of passive reinforcement and cross-

## sectional dimensions

The thickness of walls forming the sides of reservoirs or tanks should generally not be less than t1 mm for class 0 or t2 mm for classes 1 or 2. Slip formed walls should not be thinner than t2 mm whatever the class and the holes left by the lifting rods should be filled with a suitable grout.

The value for t1 is 120 mm and for t2 is 150 mm.

# DECISION ON USE OF THE INFORMATIVE ANNEXES K, L, M AND N

## Annex K

Annex K may be used

## Annex L

Annex L may be used

## Annex M

Annex M may be used

## Annex N

Annex N may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None