NATIONAL ANNEX

TO

CYS EN 1993-1-6:2007/A1: 2017/AC: 2009) Eurocode 3: Design of steel structures

Part 1-6: Strength and Stability of Shell Structures

DRAFT FOR PUBLIC ENQUIRY

Prepared by: CYS/TC18 EUROCODES COMMITTEE

Cyprus Organization of Standardization

INTRODUCTION

This National Annex has been prepared by CYS/TC18Committee of the Cyprus Organization of Standardization.

# SCOPE

This National Annex is to be used together with CYS EN 1993-1-6:2007 (Including A1:2017, Corrigendum AC:2009). Any reference in the rest of this text to CYS EN 1993-1-6:2007 means the above document.

.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1993-1-6: 2007  where National choice is allowed (see Section NA 2):

3.1(4)

4.1.4(3)

5.2.4(1)

6.2.1(6)

6.3(5)

7.3.1(1)

7.3.2(1)

8.4.2(3)

8.4.3(2)

8.4.3(4)

8.4.4(4)

8.4.5(1)

8.5.2(2)

8.5.2(4)

8.6.3(5)

8.8.2(9)

8.8.2(18)

8.8.2(20) (2 times)

9.2.1(2)P

References to non-contradictory complementary information to assist the user to apply CYS EN 1993-1-6: 2007(see Section NA 3).

# NATIONALLY DETERMINED PARAMETERS

## Clause 3.1(4) Material properties

No information is given on material properties at temperatures exceeding 150°C.

## Clause 4.1.4(3) LS4: Fatigue

The recommended value of Nf  = 10 000  shall be used.

## Clause 5.2.4(1) Stress resultants and stresses

The recommended value of the radius to thickness ratio (r/t)min  =  25  shall be used.

## Clause 6.2.1(6) Design values of stresses

## The recommended value of j =  3  shall be used.

## Clause 6.3(5) Design by global numerical MNA or GMNA analysis

The recommended value of , where fyd is in MPa, shall be used.

## Clause 7.3.1(1) Design values of total accumulated plastic strain

No recommendation is given for a more refined materially nonlinear global analysis.

## Clause 7.3.2(1) Total accumulated plastic strain limitation

The recommended value of  np,eq  =  25  for use in equation (7.5) of CYS EN 1993-1-6: 2007  shall be used.

## Clause 8.4.2(3) Out-of-roundness tolerance

Values for the out-of-roundness tolerance parameter Ur,max as recommended in Table 8.1 of CYS EN 1993-1-6: 2007  are given in Table 8.1 (CYS).

Table 8.1 (CYS): Values for out-of-roundness tolerance parameter  Ur,max

|  | Diameter range | d[m]  0,50m | 0,50m < d[m] < 1,25m | 1,25m  d[m] |
| --- | --- | --- | --- | --- |
| Fabrication tolerance quality class | Description | Recommended value of Ur,max |
| Class A | Excellent | 0,014 | 0,007 + 0,0093(1,25−d) | 0,007 |
| Class B | High | 0,020 | 0,010 + 0,0133(1,25−d) | 0,010 |
| Class C | Normal | 0,030 | 0,015 + 0,0200(1,25−d) | 0,015 |

## Clause 8.4.3(2) Non-intended eccentricity tolerance

Values for the maximum permitted non-intended eccentricity ea,max as recommended in Table 8.2 of CYS EN 1993-1-6: 2007 are given in Table 8.2 (CYS).

Table 8.2 (CYS): Values for maximum permitted non-intended eccentricities

| Fabrication tolerance quality class | Description | Recommended values for maximum permitted non-intended eccentricity ea,max |
| --- | --- | --- |
| Class A | Excellent | 2 mm |
| Class B | High | 3 mm |
| Class C | Normal | 4 mm |

## Clause 8.4.3(4) Non-intended eccentricity tolerance

Values for the non-intended eccentricity tolerance parameter Ue,max as recommended in Table 8.3 of CYS EN 1993-1-6: 2007 are given in Table 8.3.

Table 8.3 (CYS): Values for non-intended  eccentricity tolerances

| Fabrication tolerance quality class | Description | Recommended value of Ue,max |
| --- | --- | --- |
| Class A | Excellent | 0,14 |
| Class B | High | 0,20 |
| Class C | Normal | 0,30 |

## Clause 8.4.4(4) Dimple tolerances

Values for the dimple tolerance parameter U0,max as recommended in Table 8.4 of CYS EN 1993-1-6: 2007are given in Table 8.4 (CYS).

Table 8.4 (CYS): Values for dimple tolerance parameter  U0,max

| Fabrication tolerance quality class | Description | Recommended value of U0.max |
| --- | --- | --- |
| Class A | Excellent | 0,006 |
| Class B | High | 0,010 |
| Class C | Normal | 0,016 |

## Clause 8.4.5(1) Interface flatness tolerance

The recommended value of   =  0,1%  =  0,001 radians shall be used.

## Clause 8.5.2(2) Design resistance (buckling strength)

Where no application standard exists for the form of construction involved, or the application standard does not define the relevant values of M1, the value of M1 shall not be taken as smaller than the recommended value of  M1 = 1,1.

## Clause 8.5.2(4) Design resistance (buckling strength)

The values of the following parameters shall be taken from Annex D of CYS EN 1993-1-6: 2007:

   	is the elastic buckling reduction factor

 	is the plastic range factor

  	is the interaction exponent

is the squash limit relative slenderness

χh	is the hardening limit

## Clause 8.6.3(5) Design value of resistance

The values of the following parameters shall be taken from Annex E of CYS EN 1993-1-6:2007:

   	is the elastic buckling reduction factor

 	is the plastic range factor

  	is the interaction exponent

is the squash limit relative slenderness

χh	is the hardening limit

## Clause 8.8.2(9) Design value of resistance

The recommended value of   = 0,1  radians shall be used.

## Clause 8.8.2(18) Design value of resistance

No additional requirements are defined for the assessment of appropriate patterns of imperfections.

## Clause 8.8.2(20) (2 times) Design value of resistance

The recommended value of  ni = 25  shall be used.

Values for the dimple tolerance parameter Un1 and Un2 as recommended in Table 8.5 of CYS EN 1993-1-6: 2007are given in Table 8.5 (CYS).

Table 8.5 (CYS): Values for dimple imperfection amplitude parameters Un1 and Un2

| Fabrication tolerance quality class | Description | Recommended value of Un1 | Recommended value of Un2 |
| --- | --- | --- | --- |
| Class A | Excellent | 0,010 | 0,010 |
| Class B | High | 0,016 | 0,016 |
| Class C | Normal | 0,025 | 0,025 |

## Clause 9.2.1(2)P General

Where no application standard exists for the form of construction involved, or the application standard does not define the relevant values of the partial factor for resistance to fatigue Mf, the value of Mf should be taken from CYS EN 1993-1-9: 2005/AC: 2009 but not smaller than Mf = 1,1.

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None

# Comments

Annex E calculates λ0

Annex E calculates λ0