NATIONAL ANNEX

TO

CYS EN 1993-1-8:2005/AC:2009 Eurocode 3: Design of steel structures

Part 1-8: Design of joints

DRAFT FOR PUBLIC ENQUIRY

Prepared by: CYS/TC18 EUROCODES COMMITTEE

Cyprus Organization of Standardization

INTRODUCTION

This National Annex has been prepared by CYS/TC18 Committee of the Cyprus Organization of Standardization.

# SCOPE

This National Annex is to be used together with CYS EN 1993-1-8: 2005 (Including Corrigendum AC:2009). Any reference in the rest of this text to CYS EN 1993-1-8:2005 means the above document.

.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1993-1-8: 2005 where National choice is allowed (see Section NA 2):

1.2.6(Group 6: Rivets)

2.2(2)

3.1.1(3)

3.4

5.2.1(2)

6.2.7.2(9)

References to non-contradictory complementary information to assist the user to apply CYS EN 1993-1-8: 2005 (see Section NA 3).

# NATIONALLY DETERMINED PARAMETERS

## Clause 1.2.6 Reference Standards, Group 6: Rivets

No further information given.

## Clause 2.2(2) General Requirements

Partial safety factors γM for joints are given in Table 2.1 (CYS) which corresponds to Table 2.1 of CYS EN 1993-1-8: 2005.

Table 2.1 (CYS): Partial safety factors for joints

| Resistance of members and cross-sections | γM0 , γM1 and γM2 see CYS EN 1993-1-1: 2005/AC: 2009/A1: 2014 |
| --- | --- |
| Resistance of bolts |  |
| Resistance of rivets |  |
| Resistance of pins | γM2 = 1,25 |
| Resistance of welds |  |
| Resistance of plates in bearing |  |
| Slip resistance - at ultimate limit state (Category C) - at serviceability limit state (Category B) | γM3 = 1,25 γM3,ser = 1,1 |
| Bearing resistance of an injection bolt | γM4 = 1,0 |
| Resistance of joints in hollow section lattice girder | γM5 = 1,0 |
| Resistance of pins at serviceability limit state | γM6,ser = 1,0 |
| Preload of high strength bolts | γM7 = 1,1 |
| Resistance of concrete | γc see CYS EN 1992-1-1: 2004 /AC2010 |

## Clause 3.1.1(3) General

The yield strength fyb and the ultimate tensile strength fub for bolt classes 4.6, 4.8, 5.6, 5.8, 6.8, 8.8 and 10.9 are given in Table 2.2 (CYS) which corresponds to Table 3.1 of CYS EN 1993-1-8: 2005. These values should be adopted as characteristic values in design calculations.

Table 2.2 (CYS): Nominal values of the yield strength fyb and the ultimate tensile strength fub for bolts

| Bolt class | 4.6 | 4.8 | 5.6 | 5.8 | 6.8 | 8.8 | 10.9 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| fyb (N/mm2) | 240 | 320 | 300 | 400 | 480 | 640 | 900 |
| fub (N/mm2) | 400 | 400 | 500 | 500 | 600 | 800 | 1000 |

## Clause 3.4 Categories of bolted connections

## No information is given on the level of preload if preload is not explicitly used in the design calculations for slip resistances but is required for execution purposes or as a quality measure (e.g. for durability).

## Clause 5.2.1(2) General

No additional information is given on the classification of joints by their stiffness and strength to that given in 5.2.2.1(2) of CYS EN 1993-1-8: 2005.

## Clause 6.2.7.2(9) Beam-to-column joints with bolted end-plate connections

No further information is given on the use of equation (6.26) of CYS EN 1993-1-8: 2005.

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None