NATIONAL ANNEX

TO

CYS EN 1993-4-2:2007/Α1:2017/ΑC:2009

Eurocode 3: Design of steel structures

Part 4-2: Tanks

Draft for Public Enquiry

Prepared by: CYS/TC18 EUROCODES COMMITTEE

Cyprus Organisation of Standardisation

INTRODUCTION

This National Annex has been prepared by the CYSTC18 Committee of the Cyprus Organisation of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1993-4-2:2007

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1993-4-2:2007 where National choice is allowed (see Section NA 2)

2.2 (1)

2.2 (3)

2.9.2.1 (1)P

2.9.2.1 (2)P

2.9.2.1 (3)P

2.9.2.2 (3)P

2.9.3 (2)

3.3 (3)

4.1.4 (3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1993-4-2:2007. In this National Annex such information is provided for the following clauses in CYS EN 1993-4-2:2007 (see Section NA 3)

None

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.2 (1) Reliability differentiation

No consequence classes for tanks are defined as a function of the location, type of stored fluid and loading, the structural form, size and operational aspects.

## Clause 2.2 (3) Reliability differentiation

Table 2.1 gives values for the classification based on the size, structural form and stored contents into Consequence Classes when all other parameters result in medium consequences, see EN 1990:2002, B.3.1.

Table 2.1 a) —Consequence Class definitions depending on contents, 
size and structural form

| Consequence Class | Design Situations |
| --- | --- |
| Consequence Class 3 | Tanks storing liquids or liquefied gases with toxic or explosive potential; All flat-bottomed tanks used to store fluids at or near the top of a building; All pedestal tanks with centroidal height Hg ≥ Hga (see Fig. 2.1b); Ground-supported water tanks with parameter U in the range U > U3a; Ground-supported tanks storing water-polluting liquids with parameter U in the range U > U3b; Ground-supported tanks storing flammable liquids with parameter U in the range U > U3c. Emergency loadings should be taken into account for these structures where necessary, see A.2.14. |
| Consequence Class 2 | All pedestal tanks not in Consequence Class 3; Ground-supported water tanks with parameter U in the range U2a < U ≤ U3a; Ground-supported tanks storing water-polluting liquids with parameter U in the range U2b < U ≤ U3b; Ground-supported tanks storing flammable liquids with parameter U in the range U2c < U ≤ U3c. |
| Consequence Class 1 | All other tanks within the scope of this standard. |

NOTE 1	The values for class boundaries are as follows:

Table 2.1 b) — Recommended values for class boundaries

| Class Boundary | Recommended Value |
| --- | --- |
| Hga | 30 m |
| U3a | 27 m |
| U3b | 24 m |
| U3c | 15 m |
| U2a | 18 m |
| U2b | 15 m |
| U2c | 10 m |

NOTE 2	For the classification by Action Assessment Classes, see EN 1991-4.

## Clause 2.9.2.1 (1)P Partial factors for actions on tanks

Table 2.1 (CYS) provides the partial factors F.

## Clause 2.9.2.1 (2)P Partial factors for actions on tanks

Table 2.1 (CYS) provides the partial factors F.

## Clause 2.9.2.1 (3)P Partial factors for actions on tanks

Table 2.1 (CYS) provides the partial factors F.

Table 2.1 (CYS): Values for the partial factors for actions on tanks for persistent and transient design situations and for accidental design situation

| design situation | liquid type | recommended values for Fin case of variable actions from liquids | recommended values for Fin case of permanent actions |
| --- | --- | --- | --- |
| liquid induced loads during operation | toxic, explosive or dangerous liquids | 1,40 | 1,35 |
|  | flammable liquids | 1,30 | 1,35 |
|  | other liquids | 1,20 | 1,35 |
| liquid induced loads during test | all liquids | 1,00 | 1,35 |
| accidental actions | all liquids | 1,00 |  |

## Clause 2.9.2.2 (3)P Partial factors for resistances

Table 2.2 (CYS) provides the numerical values of partial factors Mi for tanks.

Table 2.2 (CYS): Numerical values for the partial factors for resistance

| (M0 = 1,00 | (M1 = 1,10 | (M2 = 1,25 |
| --- | --- | --- |
| (M4 = 1,00 | (M5 = 1,25 | (M6 = 1,10 |

## Clause 2.9.3 (2) Serviceability limit states

The value for the partial factor for serviceability (Mser is specified as (Mser= 1.

## Clause 3.3 (3) Steels for pressure purposes

No further information is provided.

## Clause 4.1.4 (3) Fatigue

The value for the number Nf of cycles is specified as Nf= 10000.

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None