NATIONAL ANNEX

TO

CYS EN 1993-4-3:2007/AC:2009 Eurocode 3: Design of steel structures

Part 4-3: Pipelines

DRAFT FOR PUBLIC ENQUIRY

Prepared by: CYS/TC18 EUROCODES COMMITTEE

Cyprus Organisation of Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS/TC18 Committee of the Cyprus Organisation of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1993-4-3:2007

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1993-4-3:2007 where National choice is allowed (see Section NA 2)

2.3 (2)

3.2 (1)P, (2)P, (3),(4)

3.3 (2), (3), (4)

3.4 (3)

4.2 (1)P

5.1.1 (2), (3), (4), (5), (6), (9), (10), (11), (12), (13)

5.2.3 (2)

5.2.4 (1)

Decisions on the use of the Informative Annexes A, B and C (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1993-4-3:2007. In this National Annex such information is provided for the following clauses in CYS EN 1993-4-3:2007 (see Section NA 4)

None

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.3 (2) Reliability differentiation

No minimum level of reliability for different types of pipelines is provided.

## Clause 3.2 (1)P Mechanical properties of pipeline steels

## The value of (M is specified as : (M= 1,00

## Clause 3.2 (2)P Mechanical properties of pipeline steels

The value Δf is specified as Δf= 50 Mpa.

## Clause 3.2 (3) Mechanical properties of pipeline steels

The value fu,min/fy,min is specified as fu,min/fy,min= 1,1.

## Clause 3.2 (4) Mechanical properties of pipeline steels

The value εu,min is specified as εu,min= 20 %.

## Clause 3.3 (2) Mechanical properties of welds

The value x is specified as x= 15 %.

## Clause 3.3 (3) Mechanical properties of welds

The value ε is specified as ε= 2 %.

## Clause 3.3 (4) Mechanical properties of welds

The value y is specified as y= 15 %.

## Clause 3.4 (3) Toughness requirements of plate materials and welds

The value z is specified as z= 0,5 %.

## Clause 4.2 (1)P Partial factors for actions

No partial safety factors are provided.

## Clause 5.1.1 (2) Simplified calculation method for ultimate limit state design

The numerical values of (F are specified as follows: (F1= 1,39; (F2= 1,50; (F3= 1,82.

## Clause 5.1.1 (3) Simplified calculation method for ultimate limit state design

The values of De / tmin are specified as follows: val240= 70; val360= 80; val415= 92; val480= 106.

## Clause 5.1.1 (4) Simplified calculation method for ultimate limit state design

The values of Dcover and Geff are specified as follows: Dcover= 2,5 m and Geff= 65 kN/m2.

## Clause 5.1.1 (5) Simplified calculation method for ultimate limit state design

The value of tspec,min is specified as tspec,min= 4,8 mm.

## Clause 5.1.1 (6) Simplified calculation method for ultimate limit state design

The values of ds and ℓ are specified as follows: ds= 100 mm and ℓ= 20 m.

## Clause 5.1.1 (9) Simplified calculation method for ultimate limit state design

The value of x is specified as x= 20.

## Clause 5.1.1 (10) Simplified calculation method for ultimate limit state design

The value of T is specified as T= 35º C.

## Clause 5.1.1 (11) Simplified calculation method for ultimate limit state design

The values of T1 and T2 are specified as follows: T1= - 40º C and T2= + 60º C.

## Clause 5.1.1 (12) Simplified calculation method for ultimate limit state design

The values of y, T3, D1, D2 and l are specified as follows: y= 20; T3= 20º C; D1= 300 mm; D2= 450 mm and ℓ= 2,0 m.

## Clause 5.1.1 (13) Simplified calculation method for ultimate limit state design

The values of z, F, D2 and De / tmin are specified as follows: z= 20; F= 1,82; D2= 450 mm; val240= 57; val360= 61; val415= 70; val480= 81.

## Clause 5.2.3 (2) LS3: Deformation

The value of x is specified as x= 0,05.

## Clause 5.2.4 (1) LS4: Fatigue

No other standards for fatigue loading are provided.

# DECISION ON USE OF THE INFORMATIVE ANNEXES

## Annex A

Annex A may be used

## Annex B

Annex B may be used

## Annex C

Annex C may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None