NATIONAL ANNEX

TO

CYS EN 1994-2:2005 (Including Corrigendum AC:2009) Eurocode 4: Design of composite steel and concrete structures

Part 2: General rules and rules for bridges

Prepared by: CYS TC 18 Eurocodes Committee

Cyprus Organisation of Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 Technical Standardisation Committee of the Cyprus Organisation of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1994-2:2005 (including Corrigendum AC:2009). Any reference in the rest of text to CYS EN 1994-1:2004 means the above document.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1994-2:2005 where National choice is allowed (see Section NA 2)

1.1.3 (3)

2.4.1.1 (1)

2.4.1.2 (5)P

2.4.1.2 (6) P

5.4.4 (1)

6.2.1.5 (9)

6.2.2.5 (3)

6.3.1 (1)

6.6.1.1 (13)

6.6.3.1 (1)

6.8.1 (3)

6.8.2 (1)

7.4.1 (4)

7.4.1. (6)

8.4.3 (3)

Decision on the use of the Informative Annex C (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1994-2:2005.  In this National Annex such information is provided for the following clauses in CYS EN 1994-2:2005 (see Section NA 4)

# NATIONALLY DETERMINED PARAMETERS

## Clause 1.1.3 (3) Scope of Part 2 of Eurocode 4

No other guidance for shear connectors is provided.

## Clause 2.4.1.1 (1) Design values of actions

The value defined for symbol γP  is set to1,0 both for favourable and unfavourable effects.

## Clause 2.4.1.2 (5)P Design values of material or product properties

The value defined for symbol γV  is set to 1,25.

## Clause 2.4.1.2 (6)P Design values of material or product properties

The value defined for symbol γMf,s  is set to 1,0

## Clause 5.4.4 (1) Combination of global and local action effects

The values defined for the combination factor ψ, are shown in Figure E.2 of Annex E of EN 1993-2.

## Clause 6.2.1.5 (9) Elastic resistance to bending

Methods (7) and (8) or Section 10 of EN 1993-1-5 may be used.

## Clause 6.2.2.5 (3) Additional rules for beams in bridges

The values defined for symbols CRd,c  is set to0,15/γC, k1is set to 0,12 and σcp,0 is set to 1,85N/mm2 .

## Clause 6.3.1 (1) Filler beam decks – Scope

No further reference for transverse filler beams is provided.

## Clause 6.6.1.1 (13) Shear connection – Basis of design

No further guidance is provided.

## Clause 6.6.3.1 (1) Headed stud connectors – Design Resistance

The value defined for symbol γV is set to1,25.

## Clause 6.8.1 (3) Fatigue – General

The value defined for symbol ks  is set to 0,75.

## Clause 6.8.2 (1) Partial factors for fatigue assessment of bridges

The value defined for symbol of γMf,s  is set to 1,0..

## Clause 7.4.1 (4) Cracking of concrete – General

The values defined for symbol wk is set to wmax found in the Note to EN 1992-2, 7.3.1 (105).

## Clause 7.4.1 (6) Cracking of concrete – General

The recommended temperature difference 20K is adopted.

## Clause 8.4.3 (3)

No further information is provided.

# DECISION ON USE OF THE INFORMATIVE ANNEX C

## Annex C

Annex C may be used.

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None