NATIONAL ANNEX

TO

CYS EN 1996-2:2006+AC:2009

Eurocode 6: Design of masonry structures

Part 2: Design considerations, selection of materials and execution of masonry

DRAFT FOR PUBLIC ENQUIRY

Prepared by: CYS/TC18 Eurocodes Committee

Cyprus Organization for Standardization

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 Standardisation Technical Committee of Cyprus Organisation for Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1996-2:2006+AC:2009.Any reference in the rest of this text to CYS EN 1996-2:2006 means the above document.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1996-2:2006+AC:2009 where National choice is allowed (see Section NA 2)

2.3.4.2(2)

3.5.3.1(1)

Decisions on the use of the Informative Annexes A, B and C (see Section NA 3)

Specific references to non-contradictory complementary information, through the following clauses.

1.1(2)P

2.3.1(1)

3.4(3)

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.3.4.2(2) Spacing of movement joints

The horizontal distance lm, between vertical movement joints in external non-load bearing unreinforced masonry walls should not exceed the values given in the following table.

Maximum horizontal distance, lm,, between vertical movement joints
for unreinforced, non-loadbearing walls

| Type of masonry | lm ( m ) |
| --- | --- |
| Clay masonry | 12 |
| Calcium silicate masonry | 8 |
| Aggregate concrete and manufactured stone masonry | 6 |
| Autoclaved aerated concrete masonry | 6 |
| Natural stone masonry | 12 |

NOTE. The maximum horizontal spacing of vertical movement joints may be increased for walls containing bed joint reinforcement conforming to CYS EN 845-3. Guidance may be obtained from the manufacturers of bed joint reinforcement.

## Clause 3.5.3.1(1) Pointing for masonry other than thin layer masonry

The value of dp is 15mm for 100mm thickness of wall.

# DECISION ON USE OF INFORMATIVE ANNEXES A, B AND C

## Annex A

Annex A may be used

## Annex B

Annex B may be used

## Annex C

Annex C may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

## Clause 1.1.(2)P Scope of Part 2 of Eurocode 6

None.

## Clause 2.3.1.(1) Detailing

None.

## Clause 3.4.(3) Permissible Deviations

Deviations of the constructed masonry from its intended position should not exceed the values given in the following table 3.1

Table 3.1(CYS) Permissible deviations for masonry elements

| Position | Maximum deviation |
| --- | --- |
| Verticality |  |
| in any one storey | ± 20 mm |
| in total height of building of three storeys or more | ± 50 mm |
| vertical alignment | ± 20 mm |
| Straightness a |  |
| in any one metre | ± 10 mm |
| in 10 metres | ± 50 mm |
| Thickness |  |
| of wall leaf b | ± 5 mm or ± 5 % of the leaf thickness whichever is the greater |
| of overall cavity wall | ± 10 mm. |
| a Deviation from straightness is measured from a straight reference line between any two points. |
| b Excluding leaves of single masonry unit width or length, where the dimensional tolerances of the masonry units govern the leaf thickness. |