NATIONAL ANNEX

TO

CYS EN 1995-1-2 :2004/AC :2009

Eurocode 5 : Design of Timber Structures

Part 1-2: General – Structural fire design

Public Enquiry

Period of Enquiry

Prepared by: EUROCODES COMMITTEE CYS TC 18

Cyprus Organisation For Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS/TC18 Standardisation Technical Committee of the Cyprus Organization of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1995-1-2:2004/AC:2009

This National Annex gives:

- Nationally determined parameters for the following clauses of CYS EN 1995-1-2:2004 where National choice is allowed (see Section NA 2)

- 2.1.3(2) Maximum temperature rise for separating function in parametric fire exposure

- 2.3(1)P	 Partial safety factor for material properties

- 2.3(2)P	 Partial safety factor for material properties

- 2.4.2(3) Reduction factor for combination of actions

- 4.2.1(1) Method for determining cross-sectional properties

- Decisions on the use of the Informative Annexes A, B, C, D, E and D (see Section NA 3)

- References to non-contradictory complementary information to assist the user to apply CYS EN 1995-1-2:2004/AC:2009 (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.1.3(2) Maximum temperature rise for separating function in parametric fire exposure

The values of ΔΘ1 = 200 K and ΔΘ2 = 240 K shall be used

## Clause 2.3 Partial safety factor for material properties

(1)P	The value for the partial safety factor for material properties shall be specified as γM,fi=1.00

(2)P	The value for the partial safety factor for material properties shall be specified as γM,fi=1.00

## Clause 2.4.2(3) Reduction factor for combination of actions

The reduction factor shall take the value of ηfi=0.6 for all cases except in the case of imposed loads according to category E given in EN 1991-2-1:2002 (areas susceptible to accumulation of goods, including access areas), when it shall be taken as ηfi=0.7.

## Clause 4.2.1(1)	Simplified rules for determining cross-sectional properties

The method given in 4.2.2 shall be used

# DECISION ON USE OF THE INFORMATIVE ANNEXES

## Annex A

Annex A may be used

## Annex B

Annex B may be used

## Annex C

Annex C may be used

## Annex D

Annex D may be used

## Annex E

Annex E may be used

## Annex F

Annex F may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None