NATIONAL ANNEX

TO

CYS EN 1995-2:2004

Eurocode 5: Design of Timber Structures

Part 2: Bridges

Public Enquiry

Period of Enquiry

Prepared by: EUROCODES COMMITTEE CYS TC 18

Cyprus Organisation For Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 Standardisation Technical Committee of the Cyprus Organisation for Standardisation

# SCOPE

This National Annex is to be used together with CYS EN 1995-2:2004. Any reference in the rest of this text to CYS EN 1995-2:2004 means the above document.

This National Annex gives:

- Nationally determined parameters for the following clauses of CYS EN 1995-2:2004 where National choice is allowed (see Section NA 2)

2.3.1.2(1)	Load-duration assignment

2.4.1		Partial factors for material properties

7.2		Limiting values for deflections

7.3.1(2)	Damping ratios

- Decisions on the use of the Informative Annexes A and B (see Section NA 3)

- References to non-contradictory complementary information to assist the user to apply CYS EN 1995-2:2004 (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.3.1.2(1) – Load-duration assignment

Load duration for actions during erection shall be regarded as short term

## Clause 2.4.1. – Partial factors for material properties

For fundamental combinations the partial factors for material properties γM shall be taken from Table 2.1 of CYS EN 1995-2:2004

For accidental combinations the value of partial factor shall be γM = 1.0

## Clause 7.2 Limiting values for deflections

The limiting values for deflections shall be taken from Table 7.1 (CYS):

Table 7.1 (CYS) – Limiting values for deflections for beams, plates and trusses

| Action | Limiting value |
| --- | --- |
| Characteristic traffic load | l/400 |
| Pedestrian load and low traffic load | l/200 |

## Clause 7.3.1(2) Damping ratios

Where no other values have been verified, the damping ratio should be taken as

ζ = 0.010 for structures without mechanical joints

ζ = 0.015 for structures with mechanical joints

# DECISION ON USE OF THE INFORMATIVE ANNEXES

## Annex A

Annex A may be used

## Annex B

Annex B may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None