NATIONAL ANNEX

TO

CYS EN 1991-1-2:2002 Including AC:2013

Eurocode 1: Actions on Structures

Part 1-2: General Actions – Actions on Structures Exposed to fire

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 Standardisation Technical Committee of the Cyprus Organisation for Standardisation.(CYS)

# SCOPE

This National Annex is to be used together with CYS EN 1991-1-2:2002including AC: 2013.Any reference in the rest of this text to CYS EN 1991-1-2:2002 means the above document.

This National Annex gives:

National determined parameters for the following clauses of CYS EN 1991-1-2:2002 where national choices is allowed (see Section NA2)

2.4(4)

3.1(10)

3.3.1.2(1) NOTE 1

3.3.1.3(1)

3.3.2(2)

4.2.2(2)

4.3.1(2)

Guidance on use of the informative Annexes A, B, C, D, E, F and G  (see Section NA 3)

References to non-contradictory complementary information applicable to buildings and civil engineering works (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.4(4) Temperature Analysis

Note 1 :The specific period of time should be obtained from annex F.

Note 2 :No Further guidance is given.

## Clause 3.1(10) Thermal action for temperature analysis

Gas temperature should adopted as nominal temperature–time curves according to 3.2

## Clause 3.3.1.2(1) Note 1 Compartment fires

No more information. Clause 3.3.1.2.(1) of the standard applies.

## Clause 3.3.1.3(1) Localized Fires

Annex C should be used for determination of thermal action from localized fires

## Clause 3.3.2(2) Fire model that should be used

The one-zone models assuming a uniform time dependent temperature distribution in the compartment should be used. The calculation method is given in Annex D.

## Clause 4.2.2(2) Mechanical action for structural analysis. Additional actions

No more information.

## Clause 4.3.1(2) Combination rules for actions

The representative value of the variable action Q1 should be considered as the quasi-permanent value ψ2,1 Q1.(Recommended Value)

# DECISION ON USE OF THE INFORMATIVE ANNEXES A, B, C, D, E, F AND G

## Annex A

Annex A may be used

## Annex B

Annex B may be used

## Annex C

Annex C may be used

## Annex D

Annex D may be used

## Annex E

Annex E may be used

## Annex F

Annex F may be used

## Annex G

Annex G may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None