NATIONAL ANNEX

TO

CYS EN 1996-1-2:2005 including AC:2010

Eurocode 6: Design of masonry structures

Part 1-2: General rules - Structural fire design

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 National Standardisation Technical Committee of Cyprus Organisation for Standardisation. (CYS)

# SCOPE

This National Annex is to be used together with CYS EN 1996-1-2:2005 including AC:2010.

Any reference in the rest of this text to CYS EN 1996-1-2:2005 means the above document.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1996-1-2:2005 including AC:2010 where National choice is allowed (see Section NA 2)

2.1.3(2)

2.2(2)

2.3(2)P

3.3.3.1(1)

3.3.3.2(1)

3.3.3.3(1)

4.5(3)

Annex B

Annex C

Decisions on the use of the Informative Annexes A, C, D, and E (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1996-1-2:2005+AC:2010. In this National Annex such information is not provided (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.1.3 Actions

(2) The values of maximum temperature rise during the decay phase are ΔΘ1 = 200Κ and ΔΘ2 = 240Κ.

## Clause 2.2 Actions

(2) The emissivity value, εm, of a masonry surface depends on the material of the masonry and is given in CYS EN 1991-1-2.

## Clause 2.3 Design values of material properties

(2)P The recommended value of γΜ,fl = 1.0 for both mechanical and thermal properties of masonry is adopted.

## Clause 3.3.3.1 Thermal elongation

(1) The thermal elongation of masonry should be determined from tests or from a database. The variation of thermal elongation with temperature for some materials is given in Annex D.

## Clause 3.3.3.2 Specific heat capacity

(1) The specific heat capacity of masonry, ca, should be determined from tests or from a database. The variation of specific heat capacity with temperature for some materials is given in Annex D.

## Clause 3.3.3.3 Thermal conductivity

(1) The thermal conductivity, λa, of masonry should be determined from tests or from a database. The variation of thermal conductivity with temperature for some materials is given in Annex D.

## Clause 4.5 Assessment by tabulated data

(3) The safety factor value for use in fire tests, γGlo are taken to be between 3 and 5.

## Clause Annex B- Tabulated fire resistance of masonry

# The recommended values of tF, lF given in Tables N.B.1 to N.B.5 are adopted.

## Clause Annex C- Simplified calculation model

# The recommended values of constant c are given in Table 1 (CYS) below.

Table 1 (CYS). Values of constant, c, and temperature θ1 and θ2 by masonry material

| Masonry units and mortar (surface unprotected) according to 1.1 (2) | Values of constant c | Temperature °C |
| --- | --- | --- |
|  |  | θ2 | θ1 |
| Clay units with general purpose mortar | ccl | 600 | 100 |
| Calcium silicate units with thin layer mortar | ccs | 500 | 100 |
| Lightweight aggregate units (pumice) with general purpose mortar | cla | 400 | 100 |
| Dense aggregate units with general purpose mortar | cda | 500 | 100 |
| Autoclaved aerated units with thin layer mortar | caac | 400 | 200 |

# DECISION ON USE OF THE INFORMATIVE ANNEXES

## Annex A

Annex A may be used

## Annex C

Annex C may be used

## Annex D

Annex D may be used

## Annex E

Annex E may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None