NATIONAL ANNEX

TO

CYS EN 1993-3-2:2006

Eurocode 3: Design of steel structures

Part 3-2: Towers, masts and chimneys – Chimneys

DRAFT FOR PUBLIC ENQUIRY

Prepared by: CYS TC 18 Eurocodes Committee

Cyprus Organisation for Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 Eurocodes Committee of the Cyprus Organisation for Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1993-3-2:2006

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1993-3-2:2006 where National choice is allowed (see Section NA 2)

2.3.3.1(1)

2.3.3.5(1)

2.6(1)

4.2(1)

5.1(1)

5.2.1(3)

6.1(1)P

6.2.1(6)

6.4.1(1)

6.4.2(1)

6.4.3(2)

7.2(1)

7.2(2)

9.1(3)

9.1(4)

9.5(1)

A.1(1)

A.2(1) (2 places)

C.2(1)

Decisions on the use of the Informative Annexes B, C, D and E (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1993-3-2:2006. In this National Annex such information is provided for the following clauses in CYS EN 1993-3-2:2006 (see Section NA 4)

None

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.3.3.1(1) Imposed loads

The characteristic imposed loads on platforms and railings are specified as

- Imposed loads on platforms:  2,0 kN/m2	... (2.1a (CYS EN 1993-3-2))

- Horizontal loads on railings:  0,5 kN/m	... (2.1b (CYS EN 1993-3-2))

## Clause 2.3.3.5(1) Ice loads

No further information is provided on ice loading.

## Clause 2.6(1) Durability

The design service life of the structure is specified as 30 years.

## Clause 4.2(1) External corrosion allowance

Table 4.1 (CYS EN 1993-3-2) provides values for the external corrosion allowance cext for normal environment.

Table 4.1 (CYS)  External corrosion allowance (cext)

| Exposure | Exposure time |
| --- | --- |
|  | First 10 years | Each additional 10 years period |
| painted carbon steel (with no planned programme for repainting) | 0 | 1 mm |
| painted carbon steel (with a planned programme for repainting) | 0 | 0 mm |
| painted carbon steel protected by insulation and waterproof cladding | 0 | 1 mm |
| unprotected carbon steel | 1,5 mm | 1 mm |
| unprotected weathering steel (see (3)) | 0,5 mm | 0,3 mm |
| unprotected stainless steel | 0 | 0 |
| unprotected inner surface of the structural shell and unprotected outer surface of the liner in a double skin or multi-flue chimney (for carbon or weathering steel) | 0,2mm | 0,1mm |

## Clause 5.1(1) Modelling of the chimney for determining action effects

No further information is provided on damping effects.

## Clause 5.2.1(3) Analysis of the structural shell

The criteria for neglecting shell effects are specified as

... (5.1 (CYS EN 1993-3-2))

where	  	is the total height

rm	is the medium radius of the shell (i.e. in the middle of the plate)

t	is the corroded plate thickness

## Clause 6.1.(1)P General

The partial factors for chimneys (M are specified as

(M0 = 1,00

(M1 = 1,10

(M2 = 1,25

## Clause 6.2.1(6) Strength verification

The limits for the opening are specified as follows:

Stress distribution may generally be deemed to be satisfied if the stiffeners project above and below the opening at least 0,8 times the spacing of the stiffeners or 0,8 times the height of the opening, whichever is the greatest and the maximum angle of the opening should be 120°.

## Clause 6.4.1(1) General

The partial factors for joints and connections in chimneys are specified in Table 2.1 (CYS EN 1993-3-2) of the National Annex of CYS EN 1993-1-8, which is repeated below.

Table 2.1 : Partial safety factors for joints

| Resistance of members and cross-sections | γM0 , γM1 and γM2 see CYS EN 1993-1-1 |
| --- | --- |
| Resistance of bolts |  |
| Resistance of rivets |  |
| Resistance of pins | γM2 = 1,25 |
| Resistance of welds |  |
| Resistance of plates in bearing |  |
| Slip resistance - for hybrid connections or connections under fatigue loading - for other design situations | γM3 = 1,25 γM3,ser = 1,1 |
| Bearing resistance of an injection bolt | γM4 = 1,0 |
| Resistance of joints in hollow section lattice girder | γM5 = 1,0 |
| Resistance of pins at serviceability limit state | γM6,ser = 1,0 |
| Preload of high strength bolts | γM7 = 1,1 |
| Resistance of concrete | γc see CYS EN 1992-1-1 |

## Clause 6.4.2(1) Flange bolted connections

No further information is provided on the design of flange bolted connections.

## Clause 6.4.3(2) Connection of chimney to the foundation or supporting structure

No further information is provided on the design of the connections to the foundations.

## Clause 7.2(1) Deflections

The limiting value of the deflection in the along-wind direction at the top of a self-supporting chimney is specified as

(max = h/50	... (7.1 (CYS EN 1993-3-2))

where h is the overall height of the chimney.

## Clause 7.2(2) Deflections

Table 7.1 (CYS EN 1993-3-2) provides limiting values of vibration amplitudes, for the reliability classes, defined in Annex A of this part.

Table 7.1: Maximum amplitudes of cross-wind vibration

| Reliability class | Limits to cross-wind vibration amplitude |
| --- | --- |
| 3 | 0,05 | times the outer diameter |
| 2 | 0,10 | times the outer diameter |
| 1 | 0,15 | times the outer diameter |

## Clause 9.1(3) General

No further information is provided on the modeling for stress analysis.

## Clause 9.1(4) General

No further information is provided.

## Clause 9.5(1) Partial factors for fatigue

The value of (Ff is 1,00.

The values for (Mf are specified in Table 3.1 (CYS EN 1993-3-2) of the National Annex of CYS EN 1993-1-9, which is repeated below.

Table 3.1: Recommended values for partial factors for fatigue strength

| Assessment method | Consequence of failure |
| --- | --- |
|  | Low consequence | High consequence |
| Damage tolerant | 1,00 | 1,15 |
| Safe life | 1,15 | 1,35 |

## Clause A.1(1) Reliability differentiation for steel chimneys

Table A.1 (CYS EN 1993-3-2) provides relevant reliability classes related to the consequences of structural failure.

Table A.1: Reliability differentiation for chimneys

| Reliability Class |  |
| --- | --- |
| 3 | Chimneys erected in strategic locations, such as nuclear power plants or in densely populated urban locations. Major chimneys in manned industrial sites where the economic and social consequences of their failure would be very high. |
| 2 | All normal chimneys at industrial sites or other locations that cannot be defined as Class 1 or Class 3. |
| 1 | Chimneys built in open countryside whose failure would not cause injury. Chimneys less than 16m high in unmanned sites. |

## Clause A.2(1) Partial factors for actions

Table A.2 (CYS EN 1993-3-2) provides numerical values of (G and (Q . for the reliability classes, defined in this Annex.

Table A.2: Partial factors for permanent and variable actions

| Type of Effect | Reliability Class | Permanent Actions | Variable Actions (Qs) |
| --- | --- | --- | --- |
| unfavourable | 3 | 1,2 | 1,6 |
|  | 2 | 1,1 | 1,4 |
|  | 1 | 1,0 | 1,2 |
| favourable | All Classes | 1,0 | 0,0 |
| Accidental situations | 1,0 | 1,0 |

No information is provided on the use of dynamic response analysis for wind actions.

## Clause C.2(1) Enhancement of fatigue strength for special quality requirements

Enhancement of fatique strength can be considered for the following details, if quality level B is applied:

- transverse splices in shell with butt welds carried out from both sides

- longitudinal splices in shell with continuous seam weld

- continuous longitudinal attachment with or without shear flow

- cruciform joints with partial penetration welds

# DECISION ON USE OF THE INFORMATIVE ANNEXES

## Annex B

Annex B may be used

## Annex C

Annex C may be used

## Annex D

Annex D may be used

## Annex E

Annex E may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None