NATIONAL ANNEX

TO

CYS EN 1999-1-3:2007/A1:2011 Eurocode 9: Design of aluminium structures

Part 1-3: Structures susceptible to fatigue

PUBLIC ENQUIRY STAGE

04/06/2019-04/08/2019

Prepared by: CYS/TC18

Cyprus Organisation of Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS/TC18 Committee of the Cyprus Organisation of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1999-1-3:2007

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1999-1-3:2007 where National choice is allowed (see Section NA 2)

2.1.1 (1)

2.2.1 (4)

2.3.1 (2)

2.3.2 (6)

2.4 (1)

3 (1)

4 (2)

5.8.1 (1)

5.8.2 (1)

6.1.3 (1)

6.2.1 (2)

6.2.1 (7)

6.2.1 (11)

E (5)

E (7)

I.2.2 (1)

I.2.3.2 (1)

I.2.4 (1).

Decisions on the use of the Informative Annexes B, C, D, E, F, G, H, I, J, K and L (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1999-1-3:2007.  In this National Annex such information is provided for the following clauses in CYS EN 1999-1-3:2007 (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.1.1 (1) General

No further conditions are specified for the application for the methods of design which are specified in this clause.

## Clause 2.2.1 (4) Safe life design

Values of  Dlim are given in L.4 for use when resistance data in Annex J is adopted.

## Clause 2.3.1 (2) Source of fatigue loading

No further rules are given for the determination of the fatigue load for cases not covered by a European standard.

## Clause 2.3.2 (6) Derivation of fatigue loading

Values of kF and kN are defined to be, kF=2, and kN=2.

## Clause 2.4 (1) Partial factors for fatigue loads

Where the fatigue loads FEk have been derived in accordance with the requirements of        CYS EN 1999-1-3:2007 clauses 2.3.1 (2) and 2.3.2, the partial factor for fatigue loads (Ff , is specified as (Ff = 1,0.

Where fatigue loads have been based on confidence limits other than those in CYS EN 1999-1-3:2007 clause 2.3.2(6), the values for partial factors on loads are given in Table 2.1. (CYS).

Table 2.1 (CYS) — Partial factors (Ff for intensity and number of cycles in the fatigue load spectrum

| kF | (Ff |
| --- | --- |
|  | kN = 0 | kN = 2 |
| 0 1 2 | 1,5 1,3 1,1 | 1,4 1,2 1,0 |

## Clause 3 (1) Materials, constituent products and connecting devices

No further data for low strength alloys and tempers is provided.

## Clause 4 (2) Durability

No further information on durability is provided.

## Clause 5.8.1 (1) General

No further information on the use of the nominal stress ranges or modified nominal stress ranges is given.

## Clause 5.8.2 (1) Design value of stress range

No further information for the values of  λi are given

## Clause 6.1.3 (1) Constructional details

The set of categories given in Annex J shall be used. No further construction details are provided.

## Clause 6.2.1 (2) Classified constructional details

The values of the partial factor (Mf for a specific constructional detail type, are given in L.4 for use when Annex J resistance data is adopted.

## Clause 6.2.1 (7) Classified constructional details

No any additional provisions are given.

## Clause 6.2.1 (11) Classified constructional details

The increase in number of categories shall not exceed 2.

## Clause E (5) Adhesively bonded joints

The value of the partial factor (Mf  for specific constructional detail types is specified to be   (Mf = 3,0.

## Clause E (7) Adhesively bonded joints

No other values are defined.

## Clause I.2.2 (1) Welded material

Fatigue strength values for welded joints of castings are not defined in the National Annex.

## Clause I.2.3.2 (1) Pinned joints

Fatigue strength values for pinned joints of castings are not defined in the National Annex.

## Clause I.2.4 (1) Adhesively bonded castings

Fatigue strength values for adhesively bonded joints in castings are not defined in the National Annex.

# DECISION ON USE OF THE INFORMATIVE ANNEXES B, C, D, E, F, G, H, I, J, K and L

## Annex B

Annex B may be used

## Annex C

Annex C may be used

## Annex D

Annex D may be used

## Annex E

Annex E may be used

## Annex F

Annex F may be used

## Annex G

Annex G may be used

## Annex H

Annex H may be used

## Annex I

Annex I may be used

## Annex J

Annex J may be used

## Annex K

Annex K may be used

## Annex L

Annex L may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None