NATIONAL ANNEX

TO

CYS EN 1999-1-4:2007/AC:2009/A1:2011 Eurocode 9: Design of aluminium structures

Part 1-4: Cold-formed structural sheeting

PUBLIC ENQUIRY STAGE

04/06/2019-04/08/2019

Prepared by: CYS/TC18

Cyprus Organisation of Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS/TC18 Committee of the Cyprus Organisation of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1999-1-4:2007

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1999-1-4:2007 where National choice is allowed (see Section NA 2)

2 (3)

2 (4)

2 (5)

3.1 (3)

7.3 (3)

A.1 (1)

A.3.4 (3)

Decision on the use of the Informative Annex B (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1999-1-4:2007.  In this National Annex such information is provided for the following clauses in CYS EN 1999-1-4:2007 (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 2 (3) Basis of design

The numerical values for Mi for buildings are defined as:

M1 = 1,10

M2= 1,25

M3= 1,25

## Clause 2 (4) Basis of design

The numerical value for M,ser for buildings is defined as:

M,ser = 1,0.

## Clause 2 (5) Basis of design

No further rules are given.

## Clause 3.1 (3) General

No further guidance is given for other aluminium materials and products.

## Clause 7.3 (3) Deflections

No certain limits are specified.

## Clause A.1 (1) General

No further information on testing and on the evaluation of test results is given.

No convection factors for existing test results to be equivalent to the outcome of standardized test according to Annex A of CYS EN1999-1-4:2007 are available.

## Clause A.3.4 (3) Design values

In the case of sheeting the value for sys is specified as sys = 1,0.

No certain value for M is specified.

# DECISION ON USE OF THE INFORMATIVE ANNEX B

## Annex B

Annex B may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None