NATIONAL ANNEX

TO

CYS EN 1995-1-1:2004/A1:2008+A2:2014+AC:2006

Eurocode 5: Design of Timber Structures

Part 1-1: General – Common rules and rules for buildings

Public Enquiry Draft

Period of Enquiry

Prepared by: EUROCODES COMMITTEE CYS TC 18

Cyprus Organisation for Standardisation

INTRODUCTION

This National Annex has been prepared by the CYS/TC18 Standardisation Technical Committee of the Cyprus Organization of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1995-1-1:2004/A1:2008+A2:2014+AC:2006. Any reference in the rest of this text to CYS EN 1995-1-1:2004 means the above document

This National Annex gives:

- Nationally determined parameters for the following clauses of CYS EN 1995-1-1:2004/A1:2008 +A2:2014+AC:2006 where National choice is allowed (see Section NA 2)

2.3.1.2(2)P

2.3.1.3(1)P

2.4.1(1)P

6.4.3(8)

7.2(2)

7.3.3(2)

8.3.1.2(4)

8.3.1.2(7)

9.2.4.1(7)

9.2.5.3(1)

10.9.2(3)

10.9.2(4)

Decisions on the use of the Informative Annexes A, B, C, and D (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1995-1-1:2004/A1:2008 (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.3.1.2(2)P Load-duration classes

Examples of load-duration assignment are given in Table 2.2(CYS) below.

Table 2.2(CYS) – Examples of load-duration assignment

| Load-duration class | Loading |
| --- | --- |
| Permanent | Self-weight Machinery, equipment and lightweight partition walls fixed permanently to the structure Earth pressure |
| Long-term | Storage loads (category E) Water tank load |
| Medium-term | Snow Uniformly distributed imposed loads on floors and balconies in categories A - D Imposed loads on garages and trafficable areas (categories F and G) Actions due to moisture variation |
| Short-term | Imposed loads on stairs Concentrated imposed load (Qk) Horizontal loads on partition walls and parapets Maintenance load or load caused by persons on a roof (category H) Vehicle loads in category E Actions due to transport vehicles Installation loads |
| Instantaneous | Wind Accidental action |

## 2.3.1.3(1) Service classes

The following table provides additional information on the assignment of structures to service classes given in (2)P,(3)P and (4)P:

| Service class | Description | Maximum Moisture Content |
| --- | --- | --- |
| 1 | Timber structures in heated rooms or in corresponding moisture conditions. Any structures in thermally insulated spaces and beams with their tension side within thermal insulation | 12% |
| 2 | Dry timber structures outdoors. Structures should be in a covered and ventilated space and well protected underneath and on the sides from getting wet. For instance, timber structures in a ground floor and cold attic space are usually included in this service class. | 20% |
| 3 | Timber structures exposed to weather, in a damp space outside or subject to the immediate effect of water. | >20% |

## 2.4.1(1)P Design value of material property

The recommended values for the partial factors γM given in Table 2.3 of EN1995-1-1 for material properties and resistances are adopted.

## 6.4.3(8) Double tapered, curved and pitched cambered beams

The recommended expression (6.54) is adopted

## 7.2(2) Limiting values for deflections of beams

The limiting values for deflections of beams are given in Table 7.2 (CYS) below

Table 7.2 (CYS) – Limiting values for deflections of beams

|  | winst | wnet,fin | wfin |
| --- | --- | --- | --- |
| Beams on two supports | l/300 to l/500 | l/250 to l/350 | l/150 to l/300 |
| Cantilevering beams | l/150 to l/250 | l/125 to l/175 | l/75 to l/150 |

The higher values refer to situations where the member does not support sensitive structures or equipment (brittle partitions, machinery etc.).

For roofs in general the higher values may be used.

For general residential floors intermediate values should be chosen.

## 7.3.3(2) Residential floors

The following values should be used for the limiting values a and b

a=1.0 mm/kN

b=120

## 8.3.1.2 Nailed timber-to-timber connections

(4)	The recommendation of 8.3.1.2(3) applies. Nails in the end grain should not be considered capable of transmitting lateral forces.

(7)	Clause 8.3.1.2(7) applies for species fir (abies alba) and Douglas fir (pseydotsuga menziesee).

## 9.2.4.1(7) General

The recommended simplified analysis of wall diaphragms is carried out using method A in accordance with clause 9.2.4.2 of CYS EN 1995-1-1:2004/A1:2008+A2:2014+AC:2006

## 9.2.5.3(1) Bracing of beam and truss systems

Table 9.2 (CYS) specifies the values of the symbols in Table 9.2 of CYS EN 1995-1-1:2004/A1:2008.

Table 9.2 (CYS) – Values of modification factors

| Modification factor | Value |
| --- | --- |
| ks | 4 |
| kf,1 | 50 |
| kf,2 | 80 |
| kf,3 | 30 |

## 10.9.2 Erection

(3)	The maximum bow, abow, permitted after installation in bay of any truss member is abow,perm=15 mm.

The maximum bow permitted in total length of chord abow,perm = min (l/300; 50 mm), where l is the length of chord.

(4)	The maximum permitted deviation of a truss from true vertical alignment adev,perm = min(10 mm + h /200; 25mm) where h is the height of the truss in the actual point, in mm.

# DECISION ON USE OF THE INFORMATIVE ANNEXES

## Annex A

Annex A may be used

## Annex B

Annex B may be used

## Annex C

Annex C may be used

## Annex D

Annex D may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None