NATIONAL ANNEX

TO

CYS EN 1991-1-6:2005 Including ΑC:2013

Eurocode 1: Actions on structures

Part 1-6: General actions – Actions during execution

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 Standardisation Technical Committee of the Cyprus Organisation for Standardisation. (CYS)

# SCOPE

This National Annex is to be used together with CYS EN 1991-1-6:2005 including ΑC:2013

Any reference in the rest of this text to CYS EN 1991-6:2006 means the above document.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1991-1-6:2005 where National choice is allowed (see Section NA 2)

| Clause | Item |
| --- | --- |
| 1.1(3) | Design rules for auxiliary construction works |
| 2.2.(4) | Note 1 Positioning of construction loads classified as free |
| 3.1(1)P | Design situation corresponding to storm conditions |
| 3.1(5) NOTE 1 NOTE 2 | Return periods for the determination of the characteristic values of variable actions during execution Minimum wind speed during execution |
| 3.1(7) | Rules for the combination of snow loads and wind actions with construction loads |
| 3.1(8) NOTE 1 | Rules concerning imperfections in the geometry of the structure |
| 3.3(2) | Criteria associated with serviceability limit states during execution |
| 3.3(6) | Serviceability requirements for auxiliary construction works |
| 4.9(6) NOTE 2 | Loads and water levels for floating ice |
| 4.10(1)P | Definition of actions due to atmospheric icing |
| 4.11.1(1) | Recommended characteristic values of construction loads Qca,and Qcb |
| 4.11.2(1) NOTE 2 | Construction loads during the casting of concrete |
| 4.12(1)P NOTE 2 | Dynamic effects due to accidental actions |
| 4.12(2) | Dynamic effects due to falls of equipment |
| 4.12 (3) | Design values of human impact loads |
| 4.13(2) | Seismic actions |
| Annex A1 A1.1(1) | Representative values of the variable actions due to construction loads |
| Annex A1 A1.3(2) | Characteristic values of equivalent horizontal forces |
| Annex A2 A2.3(1) Note 1 | Design values of vertical deflections for the incremental launching of bridges. |
| Annex A2 A2.4(2) | Reduction of the characteristic value of snow loads |
| Annex A2 A2.4(3) | Reduced values of characteristic snow loads for the verification of static equilibrium |
| Annex A2 A2.5(2) | Design values of horizontal friction forces |
| Annex A2 A2.5(3) | Determination of friction coefficients min and max |

Decision on the use of the Informative Annex B (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1991-1-6:2005.  In this National Annex such information is provided for the following clauses in CYS EN 1991-1-6:2005 (see Section NA 4)

# NATIONALLY DETERMINED PARAMETERS

## Clause 1.1 (3) Design rules for auxiliary construction works

No further information is provided. Guidance may be found in the relevant European Standards.

## Clause 2.2 (4). Note 1 Positioning of construction loads classified as free

No further information is provided.

## Clause 3.1 (1)P Design situation corresponding to storm conditions

## The accidental design situation is adopted for wind actions during storm conditions, as recommended.

## Clause 3.1 (5) NOTE 1 Return periods for the determination of the characteristic values of variable actions during execution

The recommended return periods of Table 3.1 shall be used.

## Clause 3.1 (5) NOTE 2 Minimum wind speed during execution

The minimum wind velocity of 20m/s for durations of up to 3 months shall be used. No provisions are specified for other durations.

## Clause 3.1 (7) Rules for the combination of snow loads and wind actions with construction loads

No further information is provided.

## Clause 3.1 (8) NOTE 1 Rules concerning imperfections in the geometry of the structure

No further information is provided.

## Clause 3.3 (2) Criteria associated with serviceability limit states during execution

No further information is provided.

## Clause 3.3 (6) Serviceability requirements for auxiliary construction works

No further information is provided.

## Clause 4.9 (6) NOTE 2 Loads and water levels for floating ice

# No further information is provided.

## No further information is provided. Clause 4.10 (1)P Definition of actions due to atmospheric icing

No further information is provided.

## Clause 4.11.1 (1) Table 4.1 Recommended characteristic values of construction loads Qca and Qcb

The recommended characteristic values given for construction loads Qca is 1,0 KN/M2  (see also 4.11.2 of CYS EN 1991-1-6:2005  . The recommended minimum value for Bridges are: qcb,k = 0,2 kN/m2 and  Fcb,k = 100 kN

## Clause 4.11.2 (1) Note 2 Construction loads during the casting of concrete

The recommended value of Table 4.2 of CYS EN 1991-1-6:2005 shall be applied

## Clause 4.12 (1)P NOTE 2 Dynamic effects due to accidental actions

## The value of 2 for the dynamic amplification factor shall be used. In specific cases a dynamic analysis is needed.

## Clause 4.12 (2) Dynamic effects due to falls of equipment

No further information is provided.

## Clause 4.12 (3) Design values of human impact loads

No further information is provided.

## Clause 4.13 (2) Seismic actions

No further information is provided.

## Annex A1 Clause A1.1 (1) Representative values of the variable actions due to construction loads

The value for ψ0=1.0 is adopted.

The minimum value that for ψ2 is 0,2.

## Annex A1 Clause A1.3 (2) Characteristic values of equivalent horizontal forces

Equivalent horizontal forces are set to 3% of the vertical loads from the most unfavourable combination of actions.

## Annex A2 Clause A2.3 (1). Note 1Design values of vertical deflections for the incremental launching of bridges

The recommendations given in NOTE 1 shall be used.

# ( 10 mm longitudinally for one bearing, the other bearings being assumed to be at the theoretical level (Figure A2.1a);

# (  ( 2,5 mm in the transverse direction for one bearing, the other bearings being assumed to be at the theoretical level (Figure A2.1b).

## Annex A2 Clause A2.4 (2) Reduction of the characteristic value of snow loads

The reduced characteristic value for snow load is set to 30% of the characteristic value for permanent design situations.

## Annex A2 Clause A2.4 (3) Reduced values of characteristic snow loads for the verification of static equilibrium

The reduced percentage value of x(%) shall be x=75% . No further provisions are specified.

## Annex A2 Clause A2.5 (2) Design values of horizontal friction forces

The recommended value of x=10% is adopted.

## Annex A2 Clause A2.5 (3) Determination of friction coefficients μmin and μmax

The values of μmin=0 and μmax=0.04 shall be used, unless more accurate values are available from tests for movements on very low friction surfaces.

# DECISION ON USE OF THE INFORMATIVE ANNEX B

## Annex B

Annex B may be used.

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None