NATIONAL ANNEX

TO

CYS EN 1991-4:2006 Including AC:2012

Eurocode 1: Actions on structures

Part 4: Silos and tanks

INTRODUCTION

# This National Annex has been prepared by the CYS TC 18 Standardisation Technical Committee of the Cyprus Organisation for Standardisation. (CYS).

# . SCOPE

This National Annex is to be used together with CYS EN 1991-4:2006 including AC:2012. Any reference in the rest of this text to CYS EN 1991-4:2006 means the above document.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1991-4:2006 where National choice is allowed (see Section NA 2)

2.5 (5)

3.6 (2)

5.2.4.3.1 (3)

5.4.1 (3)

5.4.1 (4)

A.4 (3)

B.2.14 (1)

Decisions on the use of the Informative Annexes A, B, F and H (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1991-4:2006.  In this National Annex such information is provided for the following clauses in CYS EN 1991-4:2006 (see Section NA 4)

# NATIONALLY DETERMINED PARAMETERS

## Clause 2.5 (5) Action assessment classification

The values defining the class boundaries are shown in Table 2.1 (CYS)

Table 2.1 (CYS) — Recommended classification of silos for action assessments

| Action Assessment Class | Description |
| --- | --- |
| Action Assessment Class 3 | Silos with capacity in excess of 10 000 tonnes Silos with capacity in excess of 1000 tonnes in which any of the following design situations occur: a) eccentric discharge with eo/dc > 0,25 (see figure 1.1b) b) squat silos with top surface eccentricity with et/dc > 0,25 |
| Action Assessment Class 2 | All silos covered by this standard and not placed in another class |
| Action Assessment Class 1 | Silos with capacity below 100 tonnes |

## Clause 3.6 (2) Principles for design for explosions

No further guidance regarding the pressure exerted on structures near the silo as a result of an explosion within it is given in this National Annex.

## Clause 5.2.4.3.1 (3). Method for Action Assessment Class 3Flow channel geometry

The values of k1, k2 and k3 are 0,25, 0,4 and 0,6 respectively.

## Clause 5.4.1 (3) Retaining Silos-Filling loads on vertical walls

The method for determining the horizontal pressure ph is given in expression (5.97):

ph = γK (1 + sinφr) zs				… (5.97)

where:

zs 	is the depth below the highest stored solid contact with the wall (see Figure 5.8 CYS);

γ	is the upper characteristic value of the unit weight of the solid;

K	is the upper characteristic value of the lateral pressure ratio for the solid;

φr 	is the angle of repose of the stored solid

Figure 5.8 (CYS):  Filling pressures in retaining silo

## 5.4.1 (4) Retaining silos- Filling loads on vertical walls

The method to be used for determining the resulting vertical force nzSk is given in expression (5.98):

nzSk = (γμK/2) (1+sinφr)zs2

where μ is the upper characteristic value of the wall friction coefficient of the solid

## Clause A.4 (3) Design situations and action combinations for Action Assessment Classes 2 and 3

The values and combinations of ψ are given in Tables A.1 (CYS), A.2 (CYS), A.3 (CYS), A.4 (CYS) and A.5 (CYS), with Accompanying Actions 2 and 3 reduced by their appropriate combination factors ψ.

Table A.1 (CYS): Design situations and action combinations to be considered

| Short title | Design situation / Dominant action 1 | Permanent actions | Accompanying Action 2 | 0,2 | Accompanying Action 3 | 0,3 |
| --- | --- | --- | --- | --- | --- | --- |
| D | Solids discharge | Self weight | Foundation settlement | 1,0 | Snow or wind or thermal | 0,6 |
|  |  |  |  |  | Imposed loads or deformation | 0,7 |
| I | Imposed loads or deformation | Self weight | Solids filling | 1,0 | Snow or wind or thermal | 0,6 |
| S | Snow | Self weight | Solids filling | 1,0 |  |  |
| WF | Wind and full | Self weight | Solids filling | 1,0 |  |  |
| WE | Wind and empty | Self weight | Solids empty | 0,0 |  |  |
| T | Thermal | Self weight | Solids filling | 1,0 |  |  |
| F | Foundation settlement | Self weight | Solids discharge | 1,0 | Snow or wind or thermal | 0,6 |
|  |  |  |  | 2,2 |  | 2,3 |
| E | Explosion | Self weight | Solids filling | 0,9 | Imposed loads or deformation | 0,3 |
| V | Vehicle impact | Self weight | Solids filling | 0,8 | Imposed loads or deformation | 0,3 |
| NOTE 1: This table refers to terms in the load combination rules of Section 6 in EN 1990. NOTE 2: The subscripts of  have the following significance: first subscript is for the type of design situation: normal combination values are 0; frequent values are 1; quasi-permanent values are 2. The second subscript refers to the load number in the combination. |

Table A.2 (CYS): "Ordinary" ultimate limit state ("Ordinary" ULS) -  design situations and action combinations to be considered

| Short title | Design situation / Leading variable action | Permanent actions | Leading variable action | Accompanying variable action 1 (main) | Accompanying variable action 2 | Accompanying variable action 3, 4, etc. |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Description | (1 | (See next column, "main") |  | Description | (0,1 | Description | (0,2 | Description | (0,3 (0,4 etc |
| D | Solids discharge | Self weight | 0,9 |  |  | Solids discharge | 1,0 | Foundation settlement | 0,7 | Snow, wind, thermal | 0,6 |
|  |  |  |  |  |  |  |  |  |  | Imposed loads, imposed deformation | 0,7 |
| I | Imposed deformation | Self weight | 0,9 |  |  | Solids filling | 1,0 | Imposed deformation | 0,7 | Snow, wind, thermal | 0,6 |
|  |  |  |  |  |  |  |  |  |  | Imposed loads | 0,7 |
| S | Snow | Self weight | 0,9 |  |  | Solids filling | 1,0 | Snow | 0,6 | Imposed loads | 0,7 |
| WF | Wind and full silo | Self weight | 0,9 |  |  | Solids filling, full silo | 1,0 | Wind | 0,6 | Imposed loads | 0,7 |
| WE | Wind and empty silo | Self weight | 0,9 |  |  | Solids, empty silo | 0,0 | Wind | 0,6 | Imposed loads | 0,7 |
| T | Thermal | Self weight | 0,9 |  |  | Solids filling | 1,0 | Thermal | 0,6 | Imposed loads | 0,7 |
| NOTE: Table A.2 should be used with expressions (6.10a) and (6.10b) in EN 1990, 6.4.3.2. |

Table A.3 (CYS): "Accidental" ultimate limit state ("Accidental" ULS) - design situations and action combinations to be considered

| Short title | Design situation / Leading variable action | Permanent actions | Leading accidental action | Accompanying variable action 1 (main) | Accompanying variable action 2 | Accompanying variable action 3, 4, etc. |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Description |  | Description |  | Description | (1,1 or (2,1 | Description | (2,2 | Description | (2,3 (2,4 etc |
| E | Explosion | Self weight |  | Blast pressure |  | Solids filling | 0,9 or 0,8 | Imposed deformation | 0,3 | Imposed loads | 0,3 |
| V | Vehicle impact | Self weight |  | Vehicle impact |  | Solids filling | 0,9 or 0,8 | Imposed deformation | 0,3 | Imposed loads | 0,3 |
| NOTE: Table A.3 should be used with expression (6.11b) in EN 1990, 6.4.3.3. |

Table A.4 (CYS): "Seismic" ultimate limit state ("Seismic" ULS) - design situations and action combinations to be considered

| Short title | Design situation / Leading variable action | Permanent actions | Leading seismic action | Accompanying variable action 1 (main) | Accompanying variable action 2 | Accompanying variable action 3, 4, etc. |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Description |  | Description |  | Description | (2,1 | Description | (2,2 | Description | (2,3 (2,4 etc |
| SF | Seismic action and full silo | Self weight |  | Seismic action (earthquake) |  | Solids filling, full silo | 0,8 | Imposed deformation | 0,3 | Imposed loads | 0,3 |
| SE | Seismic action and empty silo | Self weight |  | Seismic action (earthquake) |  | Solids, empty silo | 0,8 | Imposed deformation | 0,3 | Imposed loads | 0,3 |
| NOTE: Table A.4 should be used with expression (6.12b) in EN 1990, 6.4.3.4 and those of EN 1998-1 and EN 1998-4. |

Table A.5 (CYS): Serviceability limit state (SLS) - design situations and action combinations to be considered

| Short title | Design situation / Leading variable action | Permanent actions | Leading variable action | Accompanying variable action 1 (main) | Accompanying variable action 2 | Accompanying variable action 3, 4, etc. |
| --- | --- | --- | --- | --- | --- | --- |
|  |  | Description |  | (See next column, "main") |  | Description | (1,1 or (2,1 | Description | (0,2 or (2,2 | Description | (0,3 (0,4 or (2,3 (2,4 etc |
| D | Solids discharge | Self weight |  |  |  | Solids discharge | 0,9 or 0,8 | Foundation settlement | 0,7 or 0,3 | Snow, wind, thermal | 0,6 or 0,0 |
|  |  |  |  |  |  |  |  |  |  | Imposed loads, imposed deformation | 0,7 or 0,3 |
| I | Imposed deformation | Self weight |  |  |  | Solids filling | 0,9 or 0,8 | Imposed deformation | 0,7 or 0,3 | Snow, wind, thermal | 0,6 or 0,0 |
|  |  |  |  |  |  |  |  |  |  | Imposed loads | 0,7 or 0,3 |
| S | Snow | Self weight |  |  |  | Solids filling | 0,9 or 0,8 | Snow | 0,6 or 0,0 | Imposed loads | 0,7 or 0,3 |
| WF | Wind and full silo | Self weight |  |  |  | Solids filling, full silo | 0,9 or 0,8 | Wind | 0,6 or 0,0 | Imposed loads | 0,7 or 0,3 |
| WE | Wind and empty | Self weight |  |  |  | Solids, empty silo | 0,0 | Wind | 0,6 or 0,0 | Imposed loads | 0,7 or 0,3 |
| T | Thermal | Self weight |  |  |  | Solids filling | 0,9 or 0,8 | Thermal | 0,6 or 0,0 | Imposed loads | 0,7 or 0,3 |
| NOTE: Table A.5 should be used with expressions (6.14b), (6.15b) and (6.16b) in EN 1990, 6.5.3 as follows: - Characteristic combination, expression (6.14b): The characteristic combination is normally used for irreversible limit states. - Frequent combination, expression (6.15b): The frequent combination is normally used for reversible limit states. - Quasi-permanent combination, expression (6.16b): The quasi-permanent combination is normally used for long-term effects and the appearance of the structure. |

## Clause B.2.14 (1) Accidental actions

The loads should include the consequences of events such as external blast, impact, adjacent external fire, explosion, leakage from the inner tank, roll over and overfilling of the inner tank.

These loads are not specified in the National Annex.  They may be specified by the client for the individual project.

# DECISION ON USE OF INFORMATIVES ANNEXES

## Annex A

Annex A is informative and may be used.

## Annex B

Annex B is informative and may be used

## Annex F

Annex F is informative and may be used

## Annex H

Annex H is informative and may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None