NATIONAL ANNEX

TO

CYS EN 1991-1-5:2005 Including AC:2009

Eurocode 1: Actions on structures

Part 1-5: General actions - Thermal actions

INTRODUCTION

This National Annex has been prepared by the CYS TC 18 Committee of the Cyprus Organization of Standardisation.

# SCOPE

This National Annex is to be used together with CYS EN 1991-1-5:2003 including AC:2009, Any reference in the rest of this text to CYS EN 1991-1-5:2003 means the above document.

This National Annex gives:

Nationally determined parameters for the following clauses of CYS EN 1991-1-5:2003/AC:2009 where National choice is allowed (see Section NA 2)

5.3(2) (Tables 5.1, 5.2 and 5.3)

6.1.1 (1)

6.1.2(2)

6.1.3.1(4)

6.1.3.2(1)P

6.1.3.3(3)

6.1.4(3)

6.1.4.1(1)

6.1.4.2(1)

6.1.4.3(1)

6.1.4.4(1)

6.1.5(1)

6.1.6(1)

6.2.1(1)P

6.2.2(1)

6.2.2(2)

7.2.1(1)P

7.5(3)

7.5(4)

A.1(1)

A.1(3)

A.2(2)

B (1) (Tables B.1, B.2 and B.3)

Guidance on the use of the Informative Annexes C and D (see Section NA 3)

References to non-contradictory complementary information to assist the user to apply CYS EN 1991-1-5:2003/AC:2009 (see Section NA 4).

# NATIONALLY DETERMINED PARAMETERS

## Clause 5.3 Determination of temperature profiles 5.3(2) (Tables 5.1, 5.2 and 5.3)

The values indicated in table 5.1 (CYS), 5.2 (CYS) and 5.3 (CYS) shall be used.

Table 5.1 (CYS): Indicative temperatures of inner environment Tin

| Season | Temperature Tin |
| --- | --- |
| Summer | T1 |
| Winter | T2 |
| NOTE: When no specific data are available the values T1 = 20 (C and T2 = 25 (C should be used. |

Table 5.2 (CYS): Indicative temperatures Tout for buildings above the ground level

| Season | Significant factor | Temperature Tout in 0C |
| --- | --- | --- |
| Summer | Relative absorptivity depending on surface colour | 0,5 bright light surface | Tmax + T3 |
|  |  | 0,7 light coloured surface | Tmax + T4 |
|  |  | 0,9 dark surface | Tmax + T5 |
| Winter | Tmin |
| NOTE: If no specific data are available the values T3 = 0(C, T4 = 2(C, and T5 = 4(C should be used, for North-East facing elements and T3 = 18(C, T4 = 30(C, and T5 = 42(C for South-West or horizontal facing elements. |

Table 5.3(CYS): Indicative temperatures Tout for underground parts of buildings

| Season | Depth below the ground level | Temperature Tout in 0C |
| --- | --- | --- |
| Summer | Less than 1 m | T6 |
|  | More than 1 m | T7 |
| Winter | Less than 1 m | T8 |
|  | More than 1 m | T9 |
| NOTE: If no specific data are available the values T6 = 8(C, T7 = 5(C, T8 = -5(C and T9 = -3(C should be used. |

## Clause 6.1.1(1) Bridge deck types

For bridge deck types other than the ones described in 6.1.1 values of the uniform temperature component and the temperature difference component for other types of bridges should be appropriately justified.

## Clause 6.1.2(2) Consideration of thermal actions

In general approach 1 shall be used which states “Representative values of thermal actions should be assessed by the uniform temperature component (see 6.1.3) and the temperature difference components (see 6.1.4).”

For appropriate occupations the simpler approach 2 shall be used. “Approach (2) The vertical temperature difference component given in 6.1.4 should generally include the non-linear component, see 4(3).”

## Clause 6.1.3.1(4) Uniform temperature component

The minimum and maximum uniform bridge temperature components, Te.min and Te.max., shall be taken from Figure 6.1 (CYS).

Figure 6.1 (CYS): Correlation between minimum/maximum shade air temperature
(Tmin/Tmax) and minimum/maximum uniform bridge temperature component (Te.min/Te.max)

NOTE 1: The values in Figure 6.1 are based on daily temperature ranges of 10oC. Such a range may be considered appropriate for most Member States.

NOTE 2: For steel truss and plate girders the maximum values given for type 1 may be reduced by 3oC.

## Clause 6.1.3.2(1)P Shade air temperature

Minimum and maximum shade air temperatures should be appropriately justified taking into account the specific location of the structure.

## Clause 6.1.3.3(3) Range of uniform bridge temperature component

Values shall be specified according to Note 2 of clause 6.1.3.3 of standard CYS EN 1991-1-5:2003

For bearings and expansion joints the maximum expansion range of the uniform bridge temperature component and the maximum contraction range of the uniform bridge temperature component, if no other provisions are required, shall be

(TN,exp + 20)oC and (TN,con + 20)oC, respectively

If the temperature at which the bearings and expansion joints are set is specified, then the maximum expansion range and the maximum contraction range should be

(TN,exp + 10)oC and (TN,con + 10)oC , respectively.

## Clause 6.1.4(3) Temperature difference components

In the case of cantilever construction, the initial temperature difference value should be appropriately justified for the specific structure.

## Clause 6.1.4.1(1) Vertical linear component (Approach 1)

The values given in Table 6.1 (CYS) shall be used for TM,heat and TM,cool

Table 6.1 (CYS): Values of linear temperature difference component for different types of bridge decks for road, foot and railway bridges

## Clause 6.1.4.2(1) Vertical temperature components with non-linear effects (Approach 2)

The values specified in Figures 6.2a, 6.2b and 6.2c of standard CYS EN 1991-1-5:2003

shall be used and are valid for 40mm surfacing depths for deck type 1 and 100mm for deck types 2 and 3.

Figure 6.2 a Temperature Differences for Bridges Decks-Type 1: Steel Decks

Figure 6.2 b: Temperature Differences for Bridge Decks-Type 2 : Composite Deck

## Clause 6.1.4.3(1) Horizontal components

If no other information is available and no indications of higher values exist, the value 5oC as a linear temperature difference between the outer edges of the bridge independent of the width of the bridge shall be used.

## Clause 6.1.4.4(1) Temperature difference components within walls of concrete box girders

A linear temperature difference of 15ºC shall be used.

## Clause 6.1.5(1) Simultaneity of uniform and temperature difference components

The values of N= 0,35 and M= 0,75 shall be used.

## Clause 6.1.6(1) Differences in the uniform temperature component between different structural elements

The recommended values for the differences in the uniform temperature component T = 15oC between main structural elements (e.g. tie and arch); and T = 10oC and 20oC for light and dark colour respectively between suspension /stay cables and deck (or tower) shall be used.

## Clause 6.2.1(1) P Consideration of thermal actions

In the design procedure an equivalent linear temperature difference shall be used.

## Clause 6.2.2(1) Temperature differences

For concrete piers (hollow or solid), the linear temperature difference 5oC between opposite outer faces shall be used.

## Clause 6.2.2(2) Temperature differences

The linear temperature difference between the inner and outer faces of 15oC shall be used.

## Clause 7.2.1(1)P Shade air temperature

Minimum and maximum shade air temperatures shall be appropriately justified taking into account the specific location of the structure.

## Clause 7.5(3) Values of temperature components (indicative values)

The linear temperature difference component value 15oC shall be used.

## Clause 7.5(4) Values of temperature components (indicative values)

In the absence of any specific information on characteristic values of the element temperature the value of the difference of temperature of 15oC shall be used.

## Clause A.1(1) General

Minimum and maximum shade air temperatures shall be appropriately justified taking into account the specific location of the structure.

## Clause 20 A.1(3) General

If no information is available T0 shall be taken as 10oC. In case of uncertainty concerning sensitivity of the bridge to T0, it is recommended that a lower and upper bound of an interval expected for T0 are considered.

## Clause A.2(2) Maximum and minimum shade air temperature values with an annual probability of being exceeded p other than 0,02

The following values shall be used:

k1  =  0,781;

k2  =  0,056;

k3  =  0,393;

k4  =  - 0,156;

## Clause B(1) (Tables B.1, B.2 and B.3) Temperature differences for various surfacing depths

The values indicated in table B.1 (CYS), B.2 (CYS) and B.3 (CYS) should be used.

Table B.1 (CYS) – Recommended values of (T for deck type 1

| Surfacing thickness | Temperature difference |
| --- | --- |
|  | Heating | Cooling |
|  | (T1 | (T2 | (T3 | (T4 | (T1 |
| mm | oC | oC | oC | oC | oC |
| unsurfaced 20 40 | 30 27 24 | 16 15 14 | 6 9 8 | 3 5 4 | 8 6 6 |

Table B.2 (CYS) – Recommended values of (T for deck type 2

| Depth of slab (h) | Surfacing thickness | Temperature difference |
| --- | --- | --- |
|  |  | Heating | Cooling |
|  |  | (T1 | (T1 |
| m | mm | oC | oC |
| 0,2 0,3 | unsurfaced waterproofed 1) 50 100 150 200 unsurfaced waterproofed 1) 50 100 150 200 | 16,5 23,0 18,0 13,0 10,5 8,5 18,5 26,5 20,5 16,0 12,5 10,0 | 5,9 5,9 4,4 3,5 2,3 1,6 9,0 9,0 6,8 5,0 3,7 2,7 |
| 1) These values represent upper bound values for dark colour |

Table B.3 (CYS) – Recommended values of (T for deck type 3

| Depth of slab (h) | Surfacing thickness | Temperature difference |
| --- | --- | --- |
|  |  | Heating | Cooling |
|  |  | (T1 | (T2 | (T3 | (T1 | (T2 | (T3 | (T4 |
| m | mm | oC | oC | oC | oC | oC | oC | oC |
| 0,2 | unsurfaced waterproofed 1) 50 100 150 200 | 12,0 19,5 13,2 8,5 5,6 3,7 | 5,0 8,5 4,9 3,5 2,5 2,0 | 0,1 0,0 0,3 0,5 0,2 0,5 | 4,7 4,7 3,1 2,0 1,1 0,5 | 1,7 1,7 1,0 0,5 0,3 0,2 | 0,0 0,0 0,2 0,5 0,7 1,0 | 0,7 0,7 1,2 1,5 1,7 1,8 |
| 0,4 | unsurfaced waterproofed 1) 50 100 150 200 | 15,2 23,6 17,2 12,0 8,5 6,2 | 4,4 6,5 4,6 3,0 2,0 1,3 | 1,2 1,0 1,4 1,5 1,2 1,0 | 9,0 9,0 6,4 4,5 3,2 2,2 | 3,5 3,5 2,3 1,4 0,9 0,5 | 0,4 0,4 0,6 1,0 1,4 1,9 | 2,9 2,9 3,2 3,5 3,8 4,0 |
| 0,6 | unsurfaced waterproofed 1) 50 100 150 200 | 15,2 23,6 17,6 13,0 9,7 7,2 | 4,0 6,0 4,0 3,0 2,2 1,5 | 1,4 1,4 1,8 2,0 1,7 1,5 | 11,8 11,8 8,7 6,5 4,9 3,6 | 4,0 4,0 2,7 1,8 1,1 0,6 | 0,9 0,9 1,2 1,5 1,7 1,9 | 4,6 4,6 4,9 5,0 5,1 5,1 |
| 0,8 | unsurfaced waterproofed 1) 50 100 150 200 | 15,4 23,6 17,8 13,5 10,0 7,5 | 4,0 5,0 4,0 3,0 2,5 2,1 | 2,0 1,4 2,1 2,5 2,0 1,5 | 12,8 12,8 9,8 7,6 5,8 4,5 | 3,3 3,3 2,4 1,7 1,3 1,0 | 0,9 0,9 1,2 1,5 1,7 1,9 | 5,6 5,6 5,8 6,0 6,2 6,0 |
| 1,0 | unsurfaced waterproofed 1) 50 100 150 200 | 15,4 23,6 17,8 13,5 10,0 7,5 | 4,0 5,0 4,0 3,0 2,5 2,1 | 2,0 1,4 2,1 2,5 2,0 1,5 | 13,4 13,4 10,3 8,0 6,2 4,3 | 3,0 3,0 2,1 1,5 1,1 0,9 | 0,9 0,9 1,2 1,5 1,7 1,9 | 6,4 6,4 6,3 6,3 6,2 5,8 |
| 1,5 | unsurfaced waterproofed 1) 50 100 150 200 | 15,4 23,6 17,8 13,5 10,0 7,5 | 4,5 5,0 4,0 3,0 2,5 2,1 | 2,0 1,4 2,1 2,5 2,0 1,5 | 13,7 13,7 10,6 8,4 6,5 5,0 | 1,0 1,0 0,7 0,5 0,4 0,3 | 0,6 0,6 0,8 1,0 1,1 1,2 | 6,7 6,7 6,6 6,5 6,2 5,6 |
| 1) These values represent upper bound values for dark colour |

# DECISION ON USE OF THE INFORMATIVE ANNEXES C AND D

## Annex C

Annex C may be used

## Annex D

Annex D may be used

# REFERENCES TO NON-CONTRADICTORY COMPLEMENTARY INFORMATION

None